## Slide 1: 2024.07.30
한성재

## Slide 2: 1강 로봇공학 개요
Revolute joint allows relative rotation between two links
Prismatic joint allows linear relative motion between two links
Degrees of Freedom: The number of joints determines the DOF of the manipulator
Reachable workspace: entire set of points reachable by the manipulator(어떻게든 닿을 수 있는 위치)
Dexterous workspace: subset of the reachable workspace that the manipulator can reach with an arbitrary orientation of the end-effector(특정 위치에 임의의 방향으로 접근 가능한 위치)

## Slide 3: 1강 로봇공학 개요
Forward Kinematics :
Determination of the position and orientation of the end-effector or tool in terms of joint variables(angle or displacement)
Tool Position
Tool Orientation

## Slide 4: 1강 로봇공학 개요
Inverse Kinematics :
Determination of the angle or displacement of the end-effector or tool in terms of joint
variables(position and orientation)
Equation
Numerical Solution
초기 각도 설정값
허용 오차 ex) 0.001

## Slide 5: 1강 로봇공학 개요
Velocity kinematics :
In other to control velocity, calculation the relationship between the velocity of the tool and the joint velocities.
Differentiation of tool position at Forward kinematics
Singular Configuration:
where there is no inverse Jacobian

## Slide 6: 1강 로봇공학 개요
Path and Trajectory Planning
Path Planning: determine a path to goal position without considering time, velocity, acceleration
Trajectory Planning: determine the time history of the manipulator along a given path

## Slide 7: 1강 로봇공학 개요
Dynamics:
Relationship between motion and forces
Rigid body dynamics
Inverse dynamics : Computes the required joint torques or forces that lead to the given robot motion
Forward dynamics : Computes robot motion from the joint torques or forces applied

## Slide 8: 1강 로봇공학 개요
Independent Joint Position Control: any coupling effects due to the motion of the other links is ether ignored or treated as a disturbance.

## Slide 9: 1강 로봇공학 개요
Force Control

## Slide 10: 1강 로봇공학 개요
Hybrid Position/Force Control

## Slide 11: 1강 로봇공학 개요
Hybrid Position/Force Control

## Slide 12: 2강 로봇좌표 변환
Rotation in the plane
Rotation matrix:
Direction vector의 크기는 항상 1임
Dot product는 항상 0임

## Slide 13: 2강 로봇좌표 변환
Rotational Transformations

## Slide 14: 2강 로봇좌표 변환
Composition of rotations

## Slide 15: 2강 로봇좌표 변환
Euler angles
Current coordinate frame
If , there are infinitely many solution

## Slide 16: 2강 로봇좌표 변환
Roll, Pitch, Yaw Angles
Fixed coordinate frame

## Slide 17: 2강 로봇좌표 변환
Homogeneous Transformations

## Slide 18: 3강 로봇좌표 변환